## Slide 1
Ambulatory
Breathing
Unit
Material
Silicon

## Slide 2
Indications :
      During resuscitation
        Birth asphyxia
        Respiratory distress
        Apnoea
        After surfactant therapy
        Paralysis of resp. muscles

## Slide 3
Contraindications:
      Meconium aspiration
      Diaphramatic hernia

## Slide 4
Parts
      Oxygen inlet
      Air inlet (reservoir is attached here)
      Self inflating silicon rubber bag
      Pop-off valve
      Fish-mouth valve
      Expiratory valve

## Slide 8
Reservoir
  used to increase the O2 concentration upto
  90-98%
  Prevents air from mixing with the oxygen in the bag
  Molecular weight of CO2 > O2

## Slide 9
MASK
    Round
    Anotomically shaped
    Cushioned (less traumatic, requires less pressure to maintain the seal)
    Uncushioned
    Size
    Should cover
      the nose upto the bridge,
      Mouth
      Tip of the chin
      Should not cover the eyes
Seal is maintained by E-C clamp technique

## Slide 10
Pop-off Valve
  Usually pops-off at 30-40 cm of H2O
  May be blocked to deliver first high pressure breath in HMD
  It prevents barotrauma
  Prevents the development of pneumothorax

## Slide 11
Sterilization
  Gluteraldehyde
  Washed with soap water and dried
  Autoclaved
Checked by blocking the outlet and pressing the bag, the pop-off valve should pop-off.

## Slide 12
Check for adequate ventilation:
      Adequate chest rise
      Improvement in pts SpO2

## Slide 13: Diff bet anesthesia bag and ambu bag

## Slide 14: Laryngoscope
Parts?
Types of blades?
Indications?
Method of use?
Size of blades?

## Slide 15
Parts
  Handle (also contains the batteries)
  Blade
Two types of blades
  Straight - miller
  Curved – Macintosh (preferred in children >8yrs)

## Slide 16
Size
Preterm & LBW - 0
Term neonates - 1
2 to 10 yrs - 2
> 10 yrs - 3
Indications
intubation
      During resuscitation
        Birth asphyxia
        Respiratory distress
        Apnoea
      MSL
      General anesthesia
      Foreign body

## Slide 17
Always check the bulb before intubating
Check batteries
Check for loose teeth

## Slide 19: E.T. Tube
Material?
Types?
Size?
Length?
Indications?
contraindications?
Drugs?

## Slide 21
    Preterm - 2 - 2.5
    Term upto 2wks 3 - 3.5
    2wks upto 6mths. 4 – 4.5
Lip to tip distance
    6 + weight <44wks
    3x ET tube size

## Slide 22
Uses
  Resuscitation
  Mechanical ventilation
  MSL
  Respiratory distress
  Life threatening croup
  General anesthesia
  Air way obstruction
Drugs
  Adrenaline
  Surfactant
  Sodabicarb is never given.
Notes: Seema

## Slide 23
Confirmation of tube placement
    Symmetrical chest rise
    Equal breath sounds
    Improved SpO2
    Xray – tip should be at the T4 level.
DOPE

## Slide 24: Oro-pharyngeal airway
Indications
Size

## Slide 25
Non patent nostril and choane
Macroglossia
Difficult to maintain airway
Size measured from the angle of mouth to the angle of the jaw

## Slide 27: Feeding tube
Size
Use

## Slide 28
Plastic tube with a blind end
Opening is present laterally proximal to the end
Outer end can be closed
Measured from tip of the nose to tragus to xiphisternum
Check proper placement before administering any fluids.

## Slide 29
Use
  Diagnostic
    Gastric lavage for AFB
    GI Bleeding
    TOF
    Chemical analysis of stomach contents
    To R/o imperforate anus
  Theraputic
    Feeding
    Medications
    Gastric decompression
    management of poisoning
    Umbilical line
  Other uses
    O2 catheter
    Tourniquet
    Urinary catheter

## Slide 30: Folley’s cath
1 year - 6-8
1-6yrs - 8-10
6-10 - 10
>10 - 12-14
Inserted by no touch technique
USES
  relieve acute retention
  To measure exact urine production
  Collection of sterile urine sample
  Bladder wash
  Post op patients
Contraindications
  Stricture
  Local infection
  Trauma
  Difficult insertion

## Slide 31
Macro-drip set | Macro-drip set | Macro-drip set | Macro-drip set
Macro-drip set | Macro-drip set | Macro-drip set | Macro-drip set
Macro-drip set | Macro-drip set | Macro-drip set | Macro-drip set
Macro-drip set | Macro-drip set | Macro-drip set | Macro-drip set